## Slide 1: Building Compilers for Reconfigurable Switches
Lavanya Jose, Lisa Yan,
Nick McKeown, and George Varghese
Research funded by AT&T, Intel, Open Networking Research Center.

## Slide 2: In the next 20 minutes
Fixed-function switch chips will be replaced by reconfigurable switch chips
We will program them using languages like P4
We need a compiler to compile P4 programs to reconfigurable switch chips.

## Slide 3: Fixed-Function Switch Chips
Queues
L2 Stage
IPv4Stage
Parser
IPv6 Stage
ACL Stage
L3
L2
Packet
Packet
Notes: Model
Fixed function
Pipeline

## Slide 4: Control Flow Graph
Queues
L2 Stage
IPv4Stage
Parser
IPv6 Stage
ACL Stage
L2 Table
IPv4 Table
IPv6 Table
ACL Table
L2
v4
v6
ACL
Control Flow Graph
Switch Pipeline
Fixed Action
Fixed Action
Action
Fixed Action
Notes: abstract .. match-action
look at packets thru .. can extract
so this fixed function chip is supposed to route v4 and v6 packets and filter them based on ACLs
but it’s so hard for me to use it in practice!

## Slide 5: Fixed-Function Switch Chips Are Limited
Can’t add new forwarding functionality
Can’t add new monitoring functionality
Notes: I can’t add new forwarding or monitoring functionality after I’ve bought the switch. The fixed pipeline fixes the control flow for the lifetime of the switch.

## Slide 6: Fixed-Function Switch Chips
Queues
L2 Stage
IPv4Stage
Parser
IPv6 Stage
ACL Stage
L2 Table
IPv4 Table
IPv6 Table
ACL Table
Fixed Action
Fixed Action
Action
Fixed Action
L2
v4
v6
ACL
Control Flow Graph
Switch Pipeline
MyEncap
?
MyEncap

## Slide 7: Fixed-Function Switch Chips Are Limited
Can’t add new forwarding functionality
Can’t add new monitoring functionality
Can’t move resources between functions
Queues
L2 Stage
IPv4Stage
Parser
IPv6 Stage
ACL Stage
Fixed Action
Fixed Action
Action
L2 Table
Fixed Action
IPv4 Table
IPv6 Table
ACL Table
Notes: There’s third reason they’re limited.. I can’t even moving resources b/n existing functions. And that comes up a lot!
Plus I end up wasting all that memory 
Why is it hard?

## Slide 8: Reconfigurable Switch Chips
Control Flow Graph
Switch Pipeline
Queues
Parser
Fixed Action
Fixed Action
Fixed Action
L2 Table
Fixed Action
IPv4 Table
IPv6 Table
ACL Table
Match Table
Match Table
Match Table
Match Table
L2
v4
v6
ACL
Action Macro
Action Macro
Action Macro
Action Macro

## Slide 9: Mapping Control Flow to Reconfigurable Chip.
Match Table
Action Macro
Queues
Parser
Match Table
Match Table
Match Table
L2 Table
IPv4 Table
IPv6 Table
ACL Table
Action Macro
Action Macro
Action Macro
L2
v4
v6
ACL
Control Flow Graph
Switch Pipeline
L2
v6
ACL
v4
L2 Action Macro
v4 Action Macro
v6 Action
ACL Action Macro

## Slide 10: Reconfigurable Switch Chips
Control Flow Graph
Switch Pipeline
Queues
Parser
L2 Table
IPv4 Table
ACL Table
IPv6
MyEncap
L2
v4
v6
ACL
MyEncap
L2 Action Macro
v4 Action Macro
ACL Action Macro
Action
MyEncap
Action
IPv4
Action
IPv4
Action
IPv6
IPv4
Action
Notes: - Adding my new forwarding function easy, since it comes before the forwarding tables, I make room for it and move v4 to stage 3
- Adding monitoring functions is easy too, I can add a monitoring action to any table
- Moving resources between functions is easy. If v6 was using even fewer entries I could reclaim that space for v4.

## Slide 11
Parser
L2 Table
IPv4 Table
IPv6 Table
ACL Table
Match
Memory
Action
ALU
Protocol Independent Switch
L2 Action Macro
v4 Action Macro
v6 Action Macro
ACL Action Macro

## Slide 12
Parser
L2 Table
IPv4 Table
IPv6
ACL Table
IPv4 Table
IPv4 Table
L2 Action Macro
v4 Action Macro
Action
Action
Action
Notes: When multiple tables share a stage in this chip, resources are split between them.

## Slide 13
Match + Action Processor: pipelined and in-parallel

## Slide 14: Reconfigurability: the norm in 5 years
Reconfigurability adds mostly to logic.
Logic is getting relatively smaller.
The cost of reconfigurability is going down.
Fixed switch chip area today:
  I/O (40%), Memory (40%),
  Wires, Logic
Switch I/O (30%)
Memory (30%)
Wires (20%)
Logic (20%)
Switch I/O
Memory
Wires
Logic

## Slide 15
Fixed Function Broadcom Tomahawk: 3.2 Tbps
Reconfigurable Cavium Xpliant: 3.2 Tbps

## Slide 16
Reconfigurable chips are inevitable.
Notes: And we gotta figure out how to configure them!

## Slide 17: Configuring Switch Chips
P4 code
Compiler
Compiler Target
Queues
Parser
Fixed Action
Fixed Action
Fixed Action
L2 Table
Fixed Action
IPv4 Table
IPv6 Table
ACL Table
Match Table
Match Table
Match Table
Match Table
Action Macro
Action Macro
Action Macro
Action Macro
Notes: There are a few packet processing languages out there like P4. So what we need is the compiler that takes a P4 program and compiles it to our compiler target- a reconfigurable switch chip!

## Slide 18: P4 (http://p4.org/)
Queues
Parser
Fixed Action
Fixed Action
Fixed Action
L2 Table
Fixed Action
IPv4 Table
IPv6 Table
ACL Table
Match Table
Match Table
Match Table
Match Table
parser parse_ethernet {
extract(ethernet);
select(latest.etherType) {
0x800 : parse_ipv4;
0x86DD : parse_ipv6;
}
}
﻿table ipv4_lpm {
reads {
ipv4.dstAddr :
lpm;
}
actions {
set_next_hop;
drop;
}
}
control ingress
{
apply(l2_table);
if (valid(ipv4)) {
apply(ipv4_table);
}
if (valid(ipv6)) {
apply(ipv6_table);
}
apply (acl);
}
L2
v4
v6
ACL
Action Macro
Action Macro
Action Macro
Action Macro
(ANCS’13)
Parser
Match Action
Tables
Control Flow Graph

## Slide 19
What does reconfigurability buy us?

## Slide 20: Benefits of Reconfigurability
Use resources efficiently
  Multiple tables per stage
  Big table in multiple stages
Use fewer stages
L2
IPv4
IPv6
ACL

## Slide 21: Naïve Mapping: Control Flow Graph
Parser
Match Table
Match Table
Match Table
Match Table
Action Macro
Action Macro
Action Macro
Action Macro
L2
v4
v6
ACL
Control Flow
Switch Pipeline
Queues
L2 Table
IPv4 Table
IPv6 Table
ACL Table
L2
v6
ACL
v4
Action
v4 Action Macro
v6 Action Macro
Action
Notes: ANIMATE
Our default approach so far, where we mapped tables one by one to a new stage, in the control flow order works. We can make sure
packet undergoes..

## Slide 22: Table Dependency Graph (TDG)
Control Flow Graph
L2
v4
v6
ACL
L2
v4
v6
ACL
Table Dependency Graph
Notes: For e.g., dep. b/n L2 and L3 because L2 must learn the source MAC to port mapping before it’s changed by L3. Thus L3 cannot start before L2.
ACL, I can make a decison to forward or drop independent of other tables...

## Slide 23: Efficient Mapping: TDG
Switch Pipeline
Queues
Parser
L2 Table
IPv4 Table
IPv6 Table
Table Dependency Graph
Control Flow Graph
L2
v4
v6
ACL
L2
v4
v6
ACL
Action
v4 Action Macro
v6 Action Macro
ACL Table
Action

## Slide 24: Resource constraints
L2
Control Flow Graph
Switch Pipeline
v4
v6
ACL
Queues
Parser
L2 Table
IPv6
IPv4
L3
L2
v6
v4
L2 Action Macro
v4 Action Macro
v6 Action Macro
Action
ACL Table

## Slide 25: More resource constraints
Header widths
Action ALU input
Memory Type
Table parallelism
Action Memory
Notes: Finally, match memories and Action ALUs aren’t the only resources we need for match action tables.
We need additional resources to make match action work, e.g., resources to carry header fields
to the match memories, to carry input data to the Action ALUs. Each such resource adds a new constraint
to the problem. So we have numerous resources constraints related to (animate!) header widths, action ALU input, ..
Not all match memories are the same- some can support any kind of lookup, others can support
only exact matches, so we need to be careful about that.

## Slide 26: The Compiler Problem
Map match action tables in a TDG to a switch pipeline while respecting dependency and resource constraints.

## Slide 27
Step 1: P4 Program
Step 2: Control Flow Graph
L2
v4
v6
ACL
Step 3: Table Dependency Graph
L2
v4
v6
ACL
Step 4: Table Configuration

## Slide 28: Is that it?

## Slide 29: Two Switches We Studied
1
2
3
4
32
…
1
4
3
5
2
RMT
32 Stages
(SIGCOMM 2013)
FlexPipe
5 Stages
(Intel FM6000)
Notes: RMT has 32 stages while FlexPipe has 5. RMT has two kinds of match memories in each stage- most support exact match only and some support ternary or longest prefix matches. FlexPipe has different kinds of memories in each stage.

## Slide 30: Additional switch features
L2
v4
v6
ACL
L2
L2
v4
v6
Table shaping in RMT
Table sharing in FlexPipe

## Slide 31: The Compiler Problem
Map match action tables in a TDG to a switch pipeline while respecting dependency and resource constraints.
Table shaping
Table sharing
Header widths
Action ALU input
Memory Type
Table parallelism
Action Memory

## Slide 32: First approach: Greedy
Prioritize one constraint
Sort tables
Map tables one at a time
Queues
Parser
1
2
3
3
Sort by
# dependencies
Notes: Different heuristics can yield different table orders depending on which constraint they prioritize.
E.g. , if we sorted by resource usage, here characterized by match width, we might have started with the wide ACL table which
needs more additional resources.

## Slide 33: First approach: Greedy
Queues
Parser
1
Prioritize one constraint
Sort tables
Map tables one at a time
2
3
4
1
1
Sort by
match width
Notes: Different heuristics can yield different table orders depending on which constraint they prioritize.
E.g., if we sorted by resource usage, here characterized by match width, instead, we might have started with the wide ACL table which
needs more additional resources.
However when there are too many constraints, it’s not clear if any of the heuristics will work.

## Slide 34: Too many constraints for Greedy
Any greedy must sort tables based on a metric that is a fixed function of constraints.
As the number of constraints gets larger, it’s harder for a fixed function to represent the interplay between all constraints.
Can we do better than greedy?

## Slide 35: Second approach: Integer Linear Programming (ILP)
Find an optimal mapping.
Pros:
Takes in all constraints
Different objectives
Solvers exist (CPLEX)
Cons:
Blackbox solver
Encoding is an art
Slow

## Slide 36: ILP Setup
min # stages
subject to:
≥
≤
dependency constraints
table sizes
assigned
memories
assigned
table sizes
specified
memories in
physical stage

## Slide 37: Experiment Setup
4 datacenter use cases from Intel, Barefoot
Differ in tables, table sizes, and dependencies

## Slide 38: Example Use Case
A Typical TDG
IPv6-Mcast
EG-ACL1
EG-Phy-Meta
IG-Agg-Intf
IG-Dmac
IPv4-Mcast
IPv4-Nexthop
IPv6-Nexthop
IG-Props
IG-Router-Mac
Ipv4-Ecmp
IG-Smac
Ipv4-Ucast-LPM
Ipv4-Ucast-Host
Ipv6-Ucast-Host
Ipv6-Ucast-LPM
Ipv6-Ecmp
IG_ACL2
IG_Bcast_Storm
Ipv4_Urpf
Ipv6_Urpf
IG_ACL1
EG_Props
IG_Phy_Meta
Configuration for RMT

## Slide 39: Metrics: Greedy vs ILP
Ability to fit program in chip
Optimality
Runtime

## Slide 40: Setup: Greedy vs ILP
Ability to fit: FlexPipe
  Variants of use cases in 5-stage pipeline.
Optimality: RMT
  Minimum stage, pipeline latency, power
Runtime: both switches
Notes: - Comparing whether the approach can actually fit- this is more of an issue for FlexPipe which has a limited number of stages and limited resources per stage. So we tried twenty different realistic variants of two of the use cases, and compared what fraction of these programs could be fit in the 5 stage pipeline by Greedy vs ILP.
Comparing optimality- When fitting is not a problem, such as in RMT which has 32 stages, we can think about comparing the two approaches in terms of different objectives like the number of stages, pipeline latency and power. We do this for RMT.
Finally we compare the runtime of the two approaches both to compile to RMT and to FlexPipe.

## Slide 41: Results: Greedy vs ILP
Can Greedy fit my program?
  Yes, if resources aplenty (RMT, 32 stages)
  No, if resources constrained (FlexPipe, 5 stages), Can’t fit 25% of programs .
How close to optimal is Greedy?
  30% more time for packet to get through RMT pipeline.
Hmm.. looks like I need ILP. How slow is it?
  100x slower than Greedy
  Reasonable if programs don’t change often.
Notes: Can Greedy fit my program?
For variants of one of our use cases, greedy couldn’t fit 25% of the programs.
How close to optimal is Greedy for the RMT switch chip?
Hmm.. looks like I need ILP. How slow is it?

## Slide 42: If we have time, we should run ILP.

## Slide 43: Use ILP to suggest best Greedy for program type.
Critical constraints
Dependency critical: 16  13 stages
Additional resource constraints less important
Critical resources
TCAM memories critical: 16  14 stages
  Results for one of our datacenter L2/L3 use cases

## Slide 44: Conclusion
Challenge: Parallelism and constraints in reconfigurable chips makes compiling difficult.
TDG: highlights parallelism in program.
ILP: better if enough time, fitting is critical, or objectives are complicated.
Best Greedy: ILP can choose via notion of critical constraints and critical resources.

## Slide 45: Thank you!
Research funded by AT&T, Intel, Open Networking Research Center.

## Slide 46: ILP Run time
Number of constraints? Not obvious. E.g., RMT
  Min. stage: few secs.
  Min. power: few secs.
  Min. pipeline latency 10x slower
Number of variables? How fine-grained is the resource assignment? E.g., FlexPipe
  One match entry at a time: many days..
  100-500 match entries at a time: < 1 hr
Notes: It’s not obvious how it scales with the number of constraints-
Minimum Stage: 12s, adding ILP constraints for power: same order, adding ILP constraints for pipeline latency: 1 order of magnitude.
We did learn that the ILP run time depends on how fine-grained our resource assignment is-
For FlexPipe, if we assigned one match entry at a time, CPLEX could take hours and even days to run. However when we assigned
100-500 match entries at a time, it became more manageable on the order of tens of minutes.